860C additional manual
TSDZ2 open source firmware v20.1C.4 for APT- 860C display
modified version of 20 beta 1 (C)

Before using the software, please read the following instructions and the display wiki carefully:
Features and configurations on display · OpenSourceEBike/TSDZ2_wiki Wiki · GitHub
This manual is a supplement only.

Important before flashing: if there is already an older version on the display, make a note of the Odometer value, so that it can be entered in the new version.
- Set assist mode
There are 5 assistance modes available, the choice is in the main screen.
POWER ASSIST	assistance proportional to the power on the pedals
TORQUE ASSIST	assistance proportional to the torque on the pedals
CADENCE ASSIST	assistance subordinated to the movement of the pedals
EMTB ASSIST	assistance with progressive percentage of the torque on the pedals
HYBRID ASSIST	combined torque + power assistance
At level 0, ON/OFF button to view the current mode, UP/DOWN button to change, ON/OFF button to confirm. Assistance values for all modes from 1 to 254, for eMTB from 1 to 20.
“Hybrid assist” is a combination of the “Torque assist” and “Power assist” modes.
The result is excellent low-cadence assistance typical of Torque mode, and the extension of high-cadence Power mode.
The assistance parameters are the same used in the two modes, combined with the same level.
- Menu items changed or added
Battery
Max current
Low cut-off
Voltage cal %
Parameter to correct the voltage value shown on the display.
Example, with a fully charged battery of nominal 36V, the voltage must be close to 42V, if it is lower try increasing the parameter one tenth at a time until reading 42V, vice versa if the displayed value is higher, the parameter must be decreased.
Resistance
Voltage est
Resistance est
Power loss est
SOC
Text
Calculation
Choice of the method for calculating the remaining battery percentage.
Auto	- soc% calculation with Wh used.
Automatic reset at power on when the soc% calculated with Wh consumed is different from that calculated with the voltage (+/- "Auto reset%"), useful when you put a not fully charged battery.
Wh	- soc% calculation with Wh used, reset only with fully charged battery (100%).
Or manual reset.
Volts	- soc% calculation with battery voltage, it is less accurate than the other methods.
It can be useful if you have two batteries of different capacity. To obtain a correct correspondence between soc% and voltage, it may be necessary to adjust the values of “Reset at voltage” and “Low cut-off”.
Reset at voltage
Battery total Wh
Used Wh
Manual reset (no/yes)
Use when putting on an incompletely charged battery or at the first power on after the flashing. In this case, “Used Wh” is calculated with reference to voltage.
When the battery is fully charged, the reset to 100% is automatic.
Auto reset %
Percentage difference (+/-) between socWh and socVolts for automatic reset at power on with "SOC Calculation" = Auto. Default 15%.
Charge cycles
Full battery charge cycles counter.
Motor
Motor voltage
Max motor power
Maximum motor power, set an adequate value to contain the motor heating and compatible with the power that the battery can deliver.
A maximum value of 500W is recommended.
Attention, it does not have to be continuous!
Motor acceleration
Acceleration of the motor.
As a first setting, use low values, then gradually increase if necessary.
Consider the values in the table as maximum values.
Set carefully, aware that setting a higher value than necessary can cause greater stress on the transmission.
Recommended values:
36 Volt motor, 36 volt battery = 35
36 Volt motor, 48 volt battery = 5
36 Volt motor, 52 volt battery = 0
48 Volt motor, 36 volt battery = 45
48 Volt motor, 48 volt battery = 35
48 Volt motor, 52 volt battery = 30
Motor deceleration
Set to zero, the default deceleration ramp is active, if set to 100% the minimum deceleration ramp (faster stop).
Field weakening
Enabled / Disabled. The field weakening function increases the motor cadence (up to 120 RPM when possible) but there is also a loss of efficiency.
If enabled, field weakening is automatically activated when the PWM value is greater than 100%.

Torque sensor
Torque ADC threshold
In addition to the initial assistance with just the push on the pedals, without rotation for an immediate start, now this function is also activated with the bike in motion, when you resume pedaling after a break.
Attention, by enabling the BOOST function at the same time, the effect increases!
This can cause greater transmission stress.
Assist w/o pedal rotation
Coast brake
Coast brake ADC
Calibration
Enabled / Disabled. Enable only after having entered the actual values of “Pedal torque ADC offset” and “Pedal torque ADC max”, obtained from the calibration.
Enabling without having entered the correct values can lead to unpredictable operations.
Calibration procedure: see "ADC torque sensor" in the "Technical" menu, enter the ADC value of the torque sensor without any push on the pedals in "Pedal torque ADC offset". Enter the ADC value of the torque sensor with the maximum thrust applied to the pedal (cyclist standing on the right pedal in horizontal position) in "Pedal torque ADC max".
Torque sensor calibration is required if the working range is limited.
“Pedal torque ADC max” - “Pedal torque ADC offset” < 140.
Caution. The ADC values of the torque sensor over time may change, check periodically.
Torque adc step
Torque conversion factor applied to the pedal with calibration disabled.
It is used to calculate the correct ratio between the assistance factor and the human power (only in "Power assist") and for the calculation of the human power to be shown on the display, the actual value obtained from the calibration can be entered.
Warning: enter the “ADC torque step calc” value with calibration disabled.
The “Torque adc step” value is inversely proportional to the ADC range of the torque sensor
Torque adc step adv
Torque conversion factor applied to the pedal with calibration enabled.
It has the same function as the previous parameter, but only with calibration enabled.
In the calculation of human power, "Torque offset adj" and "Torque range adj" are also evaluated.
Do not use to change the amplification of the assistance levels, for this purpose use "Torque range adj".
An optional weight calibration is also provided for this parameter.
Warning: enter the “ADC torque step calc” value with calibration enabled.
The value of “Torque adc step adv” is constant, independent of the ADC range of the torque sensor.
Torque offset adj
Parameter for adjusting the ADC offset of the torque sensor.
Values from 0 to 34, default value 20 (neutral).
When you need to increase the sensitivity at the start, for example with a hand-bike, set a value lower than 20. Warning, a value that is too low can cause an undesired start and / or a delayed stop of the motor.
If, on the other hand, you want to decrease the sensitivity at the start, set a value greater than 20.
With a value less than 20 it is recommended to disable “Assist without pedaling” and “Startup boost”.
Torque range adj
Parameter for adjusting the ADC range of the torque sensor.
Values from 0 to 40, default value 20 (neutral).
A value below 20 decreases the amplification of the range, a value greater than 20 increases it. This variation has an effect at all levels in torque sensing modes.
Necessary first, enable the torque sensor calibration and enter the actual values of “Torque ADC offset” and “Torque ADC max”.
The range value is fixed at 160 (133 with 0, 186 with 40).
Torque angle adj
Parameter for adjusting the initial angle of the torque sensor curve. Value from 0 to 40, default value 20 (neutral).
Try 20, then adjust to “feel”. With a value below 20, more gradual response and less consumption. With a value greater than 20, more reactive but with higher consumption. See the explanatory chart.
This variation has an effect at all levels in torque sensing modes.
It is necessary to first enable the torque sensor calibration and enter the actual values of “Pedal torque ADC offset” and “Pedal torque ADC max”.
With a value greater than 20, it is advisable to disable "Startup boost".
Torque adc offset
ADC value of the torque sensor without any push on the pedals.
It is obtained from the calibration procedure to be carried out on the display.
Do not use to modify the sensitivity of torque sensor on startup, for this purpose use “Torque offset adj”.

Torque adc max
# ADC value of the torque sensor with the maximum thrust applied to the pedal (cyclist standing, on the right pedal in horizontal position).
# It is obtained from the calibration procedure to be carried out on the display.
# Do not use to change the amplification of the torque sensor range, for this purpose use "Torque range adj".
Weight on pedal
Weight to be applied to the pedal for the calibration of the ADC value of the torque sensor used in the calculation of the human power to be shown on the display.
Use a weight of 20 to 25Kg.
Torque adc on weight
ADC value of the torque sensor for the calculation of human power to be shown on the display. It is not used for the calculation of the assistance factor.
It is obtained from the calibration with a weight from 20 to 30Kg, to be carried out on the display.
Calibration procedure: see "ADC torque sensor" in the "Technical" menu, enter the value read, with the weight applied to the pedals in a horizontal position, in "Torque adc on weight".
ADC torque step calc
Conversion factor of the torque applied to the pedal obtained from the calibration with the weight or from the calculation of the estimated value.
It can be used for the calculation of the human power shown on the display and for a correct ratio in the assistance calculation (only in "Power assist").
Warning: with calibration enabled or disabled, the calculated value is different.
With calibration disabled, enter the value in the “ADC torque step” parameter.
With calibration enabled, enter the value in the “ADC torque step adv” parameter.
Default weight (no/yes)
After having entered the calibration values in "Torque ADC offset" and "Torque ADC max", with this function it is possible to calculate an estimated value of "Torque adc on weight" and "ADC torque step calc" with a weight of 25Kg. The values are less accurate than those obtained with real calibration, but are adequate for the purpose.
Assist level
Number of assist levels
Power assist
“Power assist” is an assistance mode proportional to the power on the pedals.
Levels available from 1 to 9. Set assistance levels according to your needs. Value% / 2, maximum 254.
For example, applying 100 Watt to the pedals, with 150 assist, the motor delivers 300 Watt.
These assistance parameters are also used in the hybrid mode.
Torque assist
“Torque assist” is an assistance mode proportional to the torque on the pedals.
Levels available from 1 to 9. The power delivered by the motor is proportional to the applied torque and the set assistance values.
Set assistance levels according to your needs. Relative values, maximum 254.
These assistance parameters are also used in the hybrid mode.
Cadence assist
“Cadence assist” is an assistance mode subject to pedal movement.
Levels available from 1 to 9.
The power supplied by the motor depends partly on the assistance values set and partly on the cadence of the pedals. Relative values, maximum 254.
It is recommended to use this assistance mode with the brake sensors installed and enabled.
eMTB assist
“eMTB assist” is an assistance mode with progressive percentage of the torque on the pedals. Levels available from 1 to 9. The power delivered by the engine is progressively proportional to the applied torque. There are 20 predefined sensitivities.
Higher values correspond to more responsive assistance, quicker to reach maximum engine power.
Walk assist
Feature (enable/disable)
Speed (da 1 a 9)
For each level, you set the speed to reach and maintain, in km / h x10 or in mph x10.
Maximum value 60 (6.0 km / h) or 37 (3.7 mph). Try low values ​​and gradually increase.
Recommended values ​​from 25 to 45 (2.5 to 4.5 km / h) or 15 to 28 (1.5 to 2.8 mph).
Starting "Walk assist" there will be an overrun of the set speed, this is an auto calibration.
It is used to define the ratio between wheel speed and engine revs, and to calculate the maximum power required in those conditions of use (gear ratio and slope to be overcome), then it stabilizes at the set speed.
The adjustment is made on the motor revolutions, therefore it remains constant even when setting undetectable speed values.
If necessary, it is possible to repeat the self-calibration, release the button and press again.
The set speed may not be achieved due to the power limitation.
With speed sensor problems, walk assist does not work properly.
By enabling on the display in the “Various” menu, “Assist with error”, walk assist will work like the previous versions, without speed control.
Cruise feature
Enable/disable the cruise function. It can only be enabled with Walk assist enabled.
By pressing the DOWN button for a long time at speeds above 9 km/h and with the function enabled, the current speed is stored and maintained for as long as the button is pressed.
Speed may not be achieved due to limited engine power.
The speed limit has priority.
It is recommended to use cruise mode with brake sensors installed.
Find out about the legal restrictions in your country.
Startup boost
Feature (enable/disable)
Startup boost torque factor
# It is used to increase the starting assistance and at low cadence.
# “Startup boost” must be enabled. Available only in "Power assist" mode.
# It works both with standing start and with resuming pedaling in motion.
# The value of this parameter is the percentage increase in torque applied to the pedals with cadence = 0. This value gradually decreases as the cadence increases, depending on the next parameter.
# Set carefully, aware that setting too high a value can cause greater stress to the transmission. Value in %, recommended 250, maximum 500.
Startup boost cadence step
# It is used to calculate the decrease in the boost torque factor as the cadence increases, until extinction.
# Recommended value 25. Limits from 10 to 50, higher value = shorter effect.
Startup boost at zero (cadence o speed)
# Startup Boost Mode:
# - Cadence It intervenes both starting from a standstill and resuming pedaling with the bike in motion.
# - Speed It only intervenes starting from a standstill, recommended for motors with coaster brake.
Startup assist (enabled/disabled)
Enabled / Disabled. It is used to start from a stationary on difficult climbs.
If enabled, it is activated by pressing the “Up” button and holding it down, start pedaling. After starting, release the button. Usage time is limited to 10 seconds.
With the button pressed, the operation is similar to the accelerator but to start you need to pedal, the power delivered depends on the level of assistance and the thrust on the pedals.
Motor temperature
Feature
Min limit
Max limit
Units
Choice of temperature measurement units
- Auto, Celsius with SI, Fahrenheit with Imperial.
- Celsius
- Fahrenheit
Street mode
Enable mode
Enable at startup
Speed limit
Motor power limit
Throttle enable
Enabling the throttle in "Street mode".
- No
- Yes
- Legal, the operation of the accelerator is subject to the movement of the pedals.
When you stop pedaling, the motor stops. It could be considered a legal mode.
Cruise enable
Enabling the cruise function in "Street mode".
- No
- Yes
- Legal, the cruise function is dependent on the movement of the pedals.
When you stop pedaling, the motor stops. It could be considered a legal mode.

Hotkey enable
Various
Lights configuration
Lights configuration. Inquire about compliance with current regulations.
Choose your preferred mode from the 9 available.
With light control ON:
0 - on
1 - flashing
2 - on and fast flashing when braking
3 - flashing and on when braking
4 - flashing and fast flashing when braking
5 - on and on during braking also with light control OFF
6 - on and fast flashing when braking even with the light control OFF
7 - flashing and switched on when braking even with the light control OFF
8 - flashing and fast flashing when braking even with the light control OFF
The braking modes are only available with the brake sensors installed.
Assist with error
Enabled / Disabled. The presence of an error disables assistance in all modes.
It is however possible to force assistance even with an error if this is caused by a problem with a sensor. Torque, cadence or speed sensor.
You will have to choose the assistance mode that does not involve the use of the faulty sensor.
Use only in case of need, with this function enabled there are limitations in assistance.
See error codes below.
Virtual throttle step
Odometer
A service
Enabled / Disabled
Enable maintenance warning when the set distance is reached.
 A service distance
Distance for maintenance warning, in km or miles.
B service
Enabled / Disabled
Enables maintenance warning when the set travel time is reached.
B service hours
Travel time for maintenance warning in hours.
Display
…
Config shortcut key (no/yes)
By enabling this function (yes), with assistance level greater than zero, it is possible to directly access the configuration menu with a long press of the M button.
Only with level = 0, long pressing of the M button activates the customization of the numerical fields and graphs in the 3 main screens.
It is always possible to access the configuration menu with the UP + DOWN + ON/OFF buttons.
Technical
ADC battery current
ADC throttle sensor
Throttle sensor
ADC torque sensor
# Torque sensor ADC values, to be used for calibration. - Value of "Torque adc offset" without any push on the pedals. - Value of "Torque adc max" with the maximum thrust applied to the pedal (standing cyclist,
# on the right pedal in a horizontal position).
# - Value of "Torque adc on weight" with a weight from 20 to 25Kg applied to the pedal. Take note of the values obtained and enter them in the items of the “Torque sensor” menu.

ADC torque delta
# ADC value of the torque sensor without offset.
It is possible to observe and analyze the variations resulting from the calibration.
ADC torque boost
# ADC value of the torque sensor without offset and with the increase of the "Startup boost" function if enabled. Only in "Power assist" mode.
Pedal cadence
PWM duty-cycle
Motor speed
Motor FOC
Hall sensors

- Error codes
Error codes and description:
E01 – MOTOR_NOT_INIT
Communication problem, the display receives data from the motor controller, but the controller does not receive it from the display. Check the wiring.
E02 - ERROR_TORQUE_SENSOR
A mechanical problem may have occurred with the torque sensor or the calibration at startup has not been performed correctly. A torque was probably applied to the pedals during power on.
Switch off and on again so that the system can recalibrate, without forcing the pedals.
If the "Torque sensor calibration" function is enabled, check on the display if the value of "Pedal torque ADC offset" with free pedals and "Pedal torque ADC max" with maximum effort, correspond to those entered.
E03 - ERROR_CADENCE_SENSOR
While pedaling, no pulses are generated by the cadence sensor, possibly faulty.
E04 - ERROR_MOTOR_BLOCKED
Motor or wheel blocked, excessive current absorption without motor rotation.
Check the cause. After 6 seconds the error disappears and the bike can be reused.
E06 - ERROR_COMMS
Communication problem between motor controller and display, check the wiring.
E08 - ERROR_SPEED_SENSOR
Faulty speed sensor or magnet too far away.